## Slide 1: Design and Simulation of an 8-Bit Arithmetic Logic Unit (ALU)
STUDENT NAME:-THUMMURU SANJAYSIDDARTHA REDDY
STUDENT NAME:-GOSU KALYAN RAM
STUDENT NAME:-AAKARSHIT SINGH
STUDENT NAME:-NARAMULA KRISHNA CHAITANYA
Project Presentation
ROLL NO. 2620080006
ROLL NO. 2620080062
ROLL NO. 2620080069
ROLL NO. 2620080094
GUIDE NAME:- Lakshmi Karthek Vankamamidi
DEPARTMENT:- B.Tech AI&DS
COLLEGE :- KLH deemed to be university
ACADEMIC YEAR:- 2026-2027

## Slide 2: Introduction
• An Arithmetic Logic Unit (ALU) is a fundamental component of a digital processor.
• It performs arithmetic operations such as addition and subtraction and logical operations such as AND, OR, XOR and NOT.
• This project focuses on designing and simulating an 8-bit ALU that processes two 8-bit binary inputs.
• The project demonstrates how individual digital circuits can be combined to form a functional processor datapath.
8-BIT ALU • DIGITAL LOGIC DESIGN
02

## Slide 3: Problem Statement
• Design an 8-bit ALU capable of performing multiple arithmetic and logical operations on two 8-bit inputs.
• The ALU must select the required operation using control/select signals and generate an 8-bit result.
• The design should also provide status information such as Carry and Zero flags where applicable.
• Manual implementation of separate circuits can become complex, so an integrated and simulated design is required for verification.
8-BIT ALU • DIGITAL LOGIC DESIGN
03

## Slide 4: Objectives
• Design an 8-bit ALU using basic digital logic concepts.
• Implement arithmetic operations such as ADD and SUBTRACT.
• Implement logical operations such as AND, OR and XOR.
• Use control/select lines to choose the required operation.
• Simulate the circuit and verify outputs for different input combinations.
• Analyze the correctness of the design using test cases and expected results.
8-BIT ALU • DIGITAL LOGIC DESIGN
04

## Slide 5: Literature Survey / Existing System
• Traditional ALUs are built from combinations of adders, subtractors, logic gates, multiplexers and control circuits.
• A ripple-carry adder is a simple approach for multi-bit addition, but carry propagation can increase delay.
• Multiplexer-based ALUs allow several operation units to share a common output path.
• Existing processor ALUs support many operations and flags, but their complete hardware is considerably more complex than an educational 8-bit design.
• This project uses a simplified architecture suitable for learning, simulation and verification.
8-BIT ALU • DIGITAL LOGIC DESIGN
05

## Slide 6: Proposed System
• The proposed system combines arithmetic and logical units into one 8-bit ALU.
• Two 8-bit operands, A and B, are supplied as inputs.
• Arithmetic Unit: performs addition and subtraction.
• Logic Unit: performs AND, OR and XOR operations.
• Multiplexer/selection logic chooses the required operation.
• The final output is an 8-bit result with optional Carry and Zero status flags.
• The design is simulated to verify functional correctness before hardware implementation.
8-BIT ALU • DIGITAL LOGIC DESIGN
06

## Slide 7: System Architecture / Block Diagram
• Input A (8-bit) ──┐
• ├──> Arithmetic Unit ──┐
• Input B (8-bit) ──┘ │
• ├──> MUX / Operation Selector ──> Result (8-bit)
• Input A (8-bit) ──┐ │
• Input B (8-bit) ──┘──> Logic Unit ──────┘
• ↑
• Select / Control Lines
• ↓
• Carry / Zero Flag Logic
8-BIT ALU • DIGITAL LOGIC DESIGN
07

## Slide 8: Methodology / Implementation
1. Define the required operations and control codes.
2. Build the 8-bit arithmetic section using full-adder stages and subtraction logic.
3. Build the 8-bit logic section using AND, OR and XOR gates.
4. Use multiplexers to select the output corresponding to the control signal.
5. Connect flag-generation logic for Carry and Zero conditions.
6. Apply test inputs in the simulator and compare simulated outputs with expected binary results.
Example operations: ADD, SUB, AND, OR, XOR.
8-BIT ALU • DIGITAL LOGIC DESIGN
08

## Slide 9: Results and Discussion
• Representative verification cases:
• • ADD: 00001111 + 00000001 = 00010000
• • SUB: 00010000 − 00000001 = 00001111
• • AND: 10101010 AND 11001100 = 10001000
• • OR: 10101010 OR 11001100 = 11101110
• • XOR: 10101010 XOR 11001100 = 01100110
• The simulation should show the selected operation producing the expected 8-bit output. Carry and Zero flags can be checked during arithmetic and zero-result test cases.
Insert your simulator screenshot here: waveform / circuit output / truth-table verification.
8-BIT ALU • DIGITAL LOGIC DESIGN
09

## Slide 10: Conclusion
• An 8-bit Arithmetic Logic Unit was designed as a combination of arithmetic, logic and selection circuits.
• The proposed ALU can perform multiple arithmetic and logical operations on 8-bit operands.
• Simulation provides a practical way to verify the design before hardware implementation.
• The project strengthens understanding of combinational logic, adders, multiplexers, control signals and processor datapaths.
• Future work can extend the ALU with more operations, additional flags, faster adders and FPGA implementation.
8-BIT ALU • DIGITAL LOGIC DESIGN
10